## Slide 1: Ureteroscopic Management of Stones: How did the indications change?
Samih Al-Hayek
LRCP (Lond), LRCS (Eng), LMSSA (Lond), MRCS, MD, FRCS (Urol)
Consultant Urological Surgeon & Associate Lecturer
Cambridge University Hospitals, UK
Turkish Urology Academy, Trabzon 7 Sep 2019

## Slide 2
1980 – ESWL (Chaussi, Dornier HM-3)
Middle ages
1900 (open surgery)
1976 - PCNL (Fernstrom and Johansson)
1998 - fURS (Marshall)
1900
1976
1980
1991
We are living now in another urological world!
1912
1981 – URS rigid
1964
1991 – First Holmium Laser
1960
1960 – First medical laser
2008
URS Robot

## Slide 3: SURGICAL STONE MANAGEMENT
  1970’s 1980’s 1990’s 2000’s s
  SWL 0% 95% 85% 60% 40%
  URS / PNL 0% 5% 15% 40% 60%
  Open surgery 100% < 1% < 1% < 1% <1%
CHANGING TREATMENT PHILOSOPHIES

## Slide 4: URS FOR RENAL CALCULI
0
1990
1996
2008
2002
50
100
Publications in Pubmed

## Slide 5: Procedures choice changed

## Slide 6: Why are we using ureteroscopy more

## Slide 7: history
First rigid ureteroscope was made in 1960
Perez Castro in 1980 proposed and promoted rigid ureterorenoscopy in the treatment of stones
fURS 1998
Perez Castro E et al ureterorrenoscopia transuretral. Un actual proceder urologico. Arch Esp Urol. 1980; 23:5

## Slide 8: Improved design furs
Smaller outer diameter
larger working channel
Impressive deflection (270-275o)
Better fibre optics are now available
Lower costs + increased safety
Low complications
Reduced LOS
High SFE
Retrograde flexible ureterorenoscopic holmium-YAG laser lithotripsy: the new gold standard
Gould DL. et.al. - Tech.Urol.;1998 Mar;4(1):22-4.

## Slide 10: Active and passive deflection

## Slide 11: Better vision digital
Digital high definition screens
Digital chips in the scope or in the tip
Better durability with stiffer shaft
Larger endoscopic field
Crystal clear images
NBI capabilities
First digital flexible ureterorenoscope: initial experience.
Mitchell S. et al.; , J.Endourol.; 2008 Jan;22(1):47-50

## Slide 12: First digital urs experience Mitchell S. et al.; , J.Endourol.; 2008 Jan;22(1):47-50

## Slide 13
Improved visibility
Fiber-optic
Digital
Notes: Indeed, nowadays we have the possibility to improve the quality of images for semirigid ureteroscopy. The digital semirigid instruments offered us a wonderful image concomitant with the advantages of durability and rigid maneuverability. Unfortunately, they are still too big (9.5 French)!
13

## Slide 14: Intra-corporal Lithotripsy
Maybe it was a bad idea to let that stone pass spontaneously

## Slide 15: Holmium LASER

## Slide 16: Wide range of adjuncts
Wolf COBRA

## Slide 17: Disposable flexible URS

## Slide 18: Rotation capability of Roboflex is better than manual.
Manually 120o rotation (We use our fingers to provide more rotation)
Robotically 440o rotation
More accurate tip deflection
By this way we can prevent twisting of the shaft and this may provide longer life time of the endoscope.
Traxer

## Slide 19: Safety and efficacy of ureteroscopic lithotripsy in obese patients
Seven studies with 131 patients
(136 renal units)
Obese patients (mean BMI 42.2)
f-URS is a safe and efficient modality for treating obese patients with calculi less than 2 cm in size
Aboumarzouk OM, et al:; BJU Int., 2012.
A systematic review of the literature

## Slide 20: f-URS for stones >2cm: A systematic review and meta-analysis Aboumarzouk OM et.al.; J. Endourol:, 2012
9 studies, 445 patients (460 renal units)
Mean stone size was 2.5 cm
Mean operative time was 82.5 minutes (28-215)
Mean SFR was 93.7% (77%-96.7%), with an average of 1.6 procedures per patient
95.7 % SFR with stones 2-3 cm
84.6 % in those >3 cm (p: 0.01)
In experienced hands, f-URS can successfully treat patients with stones > 2 cm with a high SFR and a low complication rate

## Slide 21: 3cm stone CT Dec 13

## Slide 22: 1st stage
Notes: 14/3 most cleard

## Slide 24: INDICATIONS IN DIFFICULT ACCESS

## Slide 25: ANTEGRADE FLEXIBLE URETEROSCOPY
Very large (>15 mm) impacted stones in the proximal ureter
When the ureter is nor amendable to retrograde manipulation
SFR of 85-100%
P.Geavlete, 2013
Notes: According to the EAU guidelines on Urolithiasis 2013, percutaneous antegrade removal of the ureteral stone is an alternative when the upper urinary tract is not available for the retrograde approach. We had some cases of very large impacted proximal stones and some patients without the possibility of retrograde manipulation.

## Slide 26
EAU Guidelines 2010

## Slide 27: Urs IN >1.5CM STONES
EAU Guidelines 2011

## Slide 28
EAU guidelines 2012

## Slide 29
EAU guidelines 2012

## Slide 30
EAU guidelines 2014- 2019

## Slide 31
EAU guidelines 2014- 2019

## Slide 33
MORBIDLY OBESE
COAGULO-PATHY
FOREIGN BODIES
CALICEAL DIVERTICULUM
URINARY DIVERSION
HARD STONES
PELVIC KIDNEY
HORSESHOE KIDNEY
BODY DEFORMITIES
Special indications of fURS and Lasers
Notes: So, what about laser lithotripsy? Starting from 1953 with ultrasonic lithotripsy we have especially to remind you the holmium laser introduced in 1995.

## Slide 34
URS FUTURE PERSPECTIVES: 3D
3
Notes: What do we have new and at the same time remarkably promising? We should mention the robotic flexible ureteroscopy for renal calculi. The initial experience from USA and India already defined some comparative studies concerning the standard manual ureteroscopy. The robotic flexible technology is improving and we are waiting for significant clinical applications.

## Slide 35: Conclusions
There has been significant improvement in the optics, maneuverability and durability of the ureteroscopes
With advanced large selection of ancillary equipments, LASER, baskets, access sheaths…
This has led to wider indications for the use of ureteroscopy performing endoluminal endourological procedures, diagnostic and therapeutic
Ureteroscopy is safe and effective mini-invasive way of treating stones in all locations of the urinary tract subject to surgeon’s experience
Further advances in technology might increase the range of URS indications and improve its safety
Notes: Choi 2012, matani 2013, monn 2015

## Slide 36: Thank You